| 1. IDENTIFICATION OF THE SUBSTANCE/PREPARATION AND THE COMPANY/UNDERTAKING |
| --- |
| GHS product identifier |
| Product Name | LIME AWAY |
| Other means of identification |
| Product Code(s) | LSR |
| UN-Number | UN1760 |
| Synonyms | LSR |
| Recommended use of the chemical and restrictions on use |
| Recommended Use | Institutional dish machine detergent |
| Uses advised against | No information available |
| Supplier's details |
| Supplier Address Envirochem, Inc 425 Whitehead Ave South River, NJ 08882 TEL: 732-238-6700 |
| Emergency telephone number |
| Emergency Telephone Number | CHEM-TEL, INC. 24 Hour Emergency Contact 1-800-255-3924 |
| 2. HAZARDS IDENTIFICATION |
| Classification |
| This chemical is considered hazardous according to the OSHA Hazard Communication Standard 2012 (29 CFR 1910.1200) |
| Acute Inhalation Toxicity - Vapors | Category 4 |
| Acute Inhalation Toxicity - Dusts and Mists | Category 4 |
| Skin Corrosion/Irritation | Category 1 Subcategory 1A |
| Serious Eye Damage/Eye Irritation | Category 1 |
| GHS Label elements, including precautionary statements |
| Emergency Overview |
| Signal Word Danger |
| Hazard Statements • Harmful if inhaled • Causes severe skin burns and eye damage |
| Appearance Clear Physical State Liquid. Odor No information available |
| Precautionary Statements |  |
|  | Prevention • Use only outdoors or in a well-ventilated area • Do not breathe dust/fume/gas/mist/vapors/spray • Wash face, hands and any exposed skin thoroughly after handling • Wear protective gloves/protective clothing/eye protection/face protection |
|  | General Advice • Immediately call a POISON CENTER or doctor/physician |
|  | Eyes • IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing • Immediately call a POISON CENTER or doctor/physician. |
|  | Skin • IF ON SKIN (or hair): Take off immediately all contaminated clothing. Rinse skin with water/shower • Wash contaminated clothing before reuse |
|  | Inhalation • IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing • Call a POISON CENTER or doctor/physician if you feel unwell |
|  | Ingestion • IF SWALLOWED: Rinse mouth. DO NOT induce vomiting |
|  | Storage • Store locked up |
|  | Disposal • Dispose of contents/container to an approved waste disposal plant |
| Hazard Not Otherwise Classified (HNOC) |
| Not applicable |
| Other information |  |
| No information available. |
| 3. COMPOSITION/INFORMATION ON INGREDIENTS |
| Synonyms | LSR |
| Chemical Name | CAS-No | Weight % | Trade secret |
| Hydrogen chloride | 7647-01-0 | 10-30 | * |
| Phosphoric acid | 7664-38-2 | 10-30 | * |
| *The exact percentage (concentration) of composition has been withheld as a trade secret. |
| 4. FIRST AID MEASURES |
| Description of necessary first-aid measures |
| Eye Contact | Rinse immediately with plenty of water, also under the eyelids, for at least 15 minutes. Immediate medical attention is required. |
| Skin Contact | Wash off immediately with soap and plenty of water. Remove and wash contaminated clothing before re-use. Immediate medical attention is required. |
| Inhalation | Move to fresh air. If breathing is difficult, give oxygen. If symptoms persist, call a physician. |
| Ingestion | Drink plenty of water. Do NOT induce vomiting. Never give anything by mouth to an unconscious person. Immediate medical attention is required. |
| Most important symptoms/effects, acute and delayed |
| Most Important Symptoms/Effects | No information available. |
| Indication of immediate medical attention and special treatment needed, if necessary |
| Notes to Physician | Treat symptomatically. |
| 5. FIRE-FIGHTING MEASURES |
| Suitable Extinguishing Media Use extinguishing measures that are appropriate to local circumstances and the surrounding environment. |
|  | Unsuitable Extinguishing Media | None |
| Specific Hazards Arising from the Chemical No information available |
|  | Explosion Data |  |
|  | Sensitivity to Mechanical Impact | None. |
|  | Sensitivity to Static Discharge | None |
| Protective Equipment and Precautions for Firefighters As in any fire, wear self-contained breathing apparatus pressure-demand, MSHA/NIOSH (approved or equivalent) and full protective gear. |
| 6. ACCIDENTAL RELEASE MEASURES |
| Personal precautions, protective equipment and emergency procedures |
| Personal Precautions | Ensure adequate ventilation. Use personal protective equipment. Avoid contact with skin, eyes and clothing. Stop leak if you can do it without risk. If spilled, take caution, as material can cause surfaces to become very slippery. |
| Environmental Precautions |
| Environmental Precautions | Dispose of contents/container to an approved waste disposal plant. |
| Methods and materials for containment and cleaning up |
| Methods for Containment | Stop leak if you can do it without risk |
| Methods for Cleaning Up | Contain spill, dilute with water and neutralize as required. Wash away small spills with plenty of water. |
| 7. HANDLING AND STORAGE |
| Precautions for safe handling |
| Handling | Handle in accordance with good industrial hygiene and safety practice. Avoid breathing vapors or mists. Use only in area provided with appropriate exhaust ventilation. In case of insufficient ventilation, wear suitable respiratory equipment. Avoid contact with skin, eyes and clothing. Wear personal protective equipment. Do not eat, drink or smoke when using this product. Do not take internally. Wash thoroughly after handling. |
| Conditions for safe storage, including any incompatibilities |
| Storage | Keep containers tightly closed in a dry, cool and well-ventilated place. Store at room temperature. Keep from freezing. Keep container closed when not in use. Keep out of the reach of children. |
| Incompatible Products | Acids. Chlorine-based bleaching agents. Oxidizing agents. Metals. Alkalis. Do not mix with anything but water |
| 8. EXPOSURE CONTROLS / PERSONAL PROTECTION |
| Control parameters |
| Exposure Guidelines |  |
| Chemical Name | ACGIH TLV | OSHA PEL | NIOSH IDLH |
| Hydrogen chloride 7647-01-0 | Ceiling: 2 ppm | (vacated) Ceiling: 5 ppm (vacated) Ceiling: 7 mg/m3 Ceiling: 5 ppm Ceiling: 7 mg/m3 | IDLH: 50 ppm Ceiling: 5 ppm Ceiling: 7 mg/m3 |
| Phosphoric acid 7664-38-2 | STEL: 3 mg/m3 TWA: 1 mg/m3 | TWA: 1 mg/m3 (vacated) TWA: 1 mg/m3 (vacated) STEL: 3 mg/m3 | IDLH: 1000 mg/m3 TWA: 1 mg/m3 STEL: 3 mg/m3 |
| Appropriate engineering controls |
| Engineering Measures | Showers Eyewash stations Ventilation systems |
| Individual protection measures, such as personal protective equipment |
| Eye/Face Protection | Tightly fitting safety goggles. |
| Skin and Body Protection | Rubber boots. Apron. Rubber gloves. Latex gloves |
| Respiratory Protection | No protective equipment is needed under normal use conditions. If exposure limits are exceeded or irritation is experienced, ventilation and evacuation may be required. |
| Hygiene Measures | Handle in accordance with good industrial hygiene and safety practice. |
| 9. PHYSICAL AND CHEMICAL PROPERTIES |
| Information on basic physical and chemical properties |
| Physical State Liquid | Appearance Clear |
| Odor No information available | Odor Threshold No information available |
| Property Values | Remarks/ - Method |
| pH 1.8 | (4 % solution) |
| Melting Point/Range No data available | None known |
| Boiling Point/Boiling Range > 100 °C / > 212 °F | None known |
| Flash Point No data available | None known |
| Evaporation rate No data available | None known |
| Flammability (solid, gas) No data available | None known |
| Flammability Limits in Air |  |
| upper flammability limit No data available |  |
| lower flammability limit No data available |  |
| Vapor Pressure No data available | None known |
| Vapor Density No data available | None known |
| Relative Density No data available | None known |
| Specific Gravity 1.09 | None known |
| Water Solubility 100% | None known |
| Solubility in other solvents No data available | None known |
| Partition coefficient: n-octanol/water No data available | None known |
| Autoignition Temperature No data available | None known |
| Decomposition Temperature No data available | None known |
| Viscosity 5 cps | None known |
| Flammable Properties | Not flammable |
| Explosive Properties | No data available |
| Oxidizing Properties | No data available |
| Other information |
| VOC Content (%) | No data available |
| 10. STABILITY AND REACTIVITY |
| Reactivity |
| No data available. |
| Chemical stability |
| Stable under recommended storage conditions. |
| Possibility of hazardous reactions |
| None under normal processing. |
| Conditions to avoid |
| Spills or careless handling. Incompatible products. |
| Incompatible materials |
| Acids. Chlorine-based bleaching agents. Oxidizing agents. Metals. Alkalis. Do not mix with anything but water |
| Hazardous decomposition products |
| None, but may liberate Hydrogen Gas in the presence of metals. |
| 11. TOXICOLOGICAL INFORMATION |
| Information on likely routes of exposure |
| Product Information |  |
|  | Inhalation | Harmful by inhalation. May cause irritation of respiratory tract. |
|  | Eye Contact | Causes serious eye damage. |
|  | Skin Contact | Causes severe skin burns. |
|  | Ingestion | May be harmful if swallowed. |
| Chemical Name | LD50 Oral | LD50 Dermal | LC50 Inhalation |
| Hydrogen chloride | = 700 mg/kg ( Rat ) | > 5010 mg/kg ( Rabbit ) | = 3124 ppm ( Rat ) 1 h |
| Phosphoric acid | = 1530 mg/kg ( Rat ) | 2730 mg/kg ( Rabbit ) | 850 mg/m3 ( Rat ) 1 h |
| Symptoms related to the physical, chemical and toxicological characteristics |
| Symptoms | No information available. |
| Delayed and immediate effects and also chronic effects from short and long term exposure |
| Sensitization | No information available. |
| Mutagenic Effects | No information available. |
| Carcinogenicity | The table below indicates whether each agency has listed any ingredient as a carcinogen. |
| Chemical Name | ACGIH | IARC | NTP | OSHA |
| Hydrogen chloride |  | Group 3 |  |  |
|  | IARC: (International Agency for Research on Cancer) Group 3: Not Classifiable as to its Carcinogenicity to Humans |
| Reproductive Toxicity | No information available. |
| STOT - single exposure | No information available. |
| STOT - repeated exposure | No information available. |
|  | Target Organ Effects | Eyes. Skin. Respiratory system. |
| Aspiration Hazard | No information available. |
| Numerical measures of toxicity - Product |
| The following values are calculated based on chapter 3.1 of the GHS document: |
| LD50 Oral | 2853 mg/kg; Acute toxicity estimate |
| LD50 Dermal | 17602 mg/kg; Acute toxicity estimate |
| Inhalation |  |
|  | dust/mist | 2.9 mg/L; Acute toxicity estimate |
|  | Vapor | 17 mg/L; Acute toxicity estimate |
| 12. ECOLOGICAL INFORMATION |
| Ecotoxicity |  |
| The environmental impact of this product has not been fully investigated. |
| Chemical Name | Toxicity to Algae | Toxicity to Fish | Toxicity to Microorganisms | Daphnia Magna (Water Flea) |
| Hydrogen chloride |  | LC50 96 h: = 282 mg/L static (Gambusia affinis) |  |  |
| Phosphoric acid |  | LC50: 3 - 3.5 mg/L Gambusia affinis 96 h |  | EC50 12 h: = 4.6 mg/L (Daphnia magna) |
| Persistence and Degradability | No information available. |
| Bioaccumulation | No information available. |
| Other Adverse Effects No information available. |
| 13. DISPOSAL CONSIDERATIONS |
| Waste Disposal Methods | Dispose of in accordance with federal, state, and local regulations |
| Contaminated Packaging | Do not re-use empty containers. |
| Chemical Name | California Hazardous Waste |
| Phosphoric acid | Corrosive |
| 14. TRANSPORT INFORMATION |
| DOT |  |
|  | UN-Number | UN1760 |
|  | Proper shipping name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Reportable Quantity (RQ) | Phosphoric acid: RQ kg= 14635.72, Hydrogen chloride: RQ kg= 13016.05 |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II, RQ |
|  | Emergency Response Guide Number | 154 |
| TDG |  |
|  | UN-Number | UN1760 |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II |
|  | UN-Number | UN1760 |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II |
| ICAO |  |
|  | UN-Number | UN1760 |
|  | Proper shipping name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Description | UN1760, Corrosive liquid, n.o.s., 8, II |
| IATA |  |
|  | UN-Number | UN1760 |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | ERG Code | 8L |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II |
| IMDG/IMO |  |
|  | UN-Number | UN1760 |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | EmS No. | F-A, S-B |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II |
| RID |  |
|  | UN-Number | UN1760 |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Classification Code | C9 |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II |
| ADR |  |
|  | UN-Number | UN1760 |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Classification Code | C9 |
| Tunnel Restriction Code | (E) |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II, (E) |
|  | ADR/RID-Labels | 8 |
| ADN |  |
|  | Proper Shipping Name | Corrosive liquid, n.o.s. |
|  | Hazard Class | 8 |
|  | Packing Group | II |
|  | Classification Code | C9 |
|  | Special Provisions | 274 |
|  | Description | UN1760, Corrosive liquid, n.o.s. (Hydrogen chloride, Phosphoric acid), 8, II |
|  | Limited Quantity | 1 L |
| 15. REGULATORY INFORMATION |
| International Inventories |  |
| TSCA | Complies |
| NDSL | Complies |
| Legend |
| TSCA - United States Toxic Substances Control Act Section 8(b) Inventory |
| DSL/NDSL - Canadian Domestic Substances List/Non-Domestic Substances List |
| U.S. Federal Regulations |  |
| Section 313 of Title III of the Superfund Amendments and Reauthorization Act of 1986 (SARA). This product contains a chemical or chemicals which are subject to the reporting requirements of the Act and Title 40 of the Code of Federal Regulations, Part 372: |
| Chemical Name | CAS-No | Weight % | SARA 313 - Threshold Values % |
| Hydrogen chloride | 7647-01-0 | 17.44 | 1.0 |
| SARA 311/312 Hazard Categories |  |
|  | Acute Health Hazard | Yes |
|  | Chronic Health Hazard | No |
|  | Fire Hazard | No |
|  | Sudden Release of Pressure Hazard | No |
|  | Reactive Hazard | No |
| Clean Water Act This product contains the following substances which are regulated pollutants pursuant to the Clean Water Act (40 CFR 122.21 and 40 CFR 122.42): |
| Chemical Name | CWA - Reportable Quantities | CWA - Toxic Pollutants | CWA - Priority Pollutants | CWA - Hazardous Substances |
| Hydrogen chloride | 5000 lb |  |  | X |
| Phosphoric acid | 5000 lb |  |  | X |
| CERCLA This material, as supplied, contains one or more substances regulated as a hazardous substance under the Comprehensive Environmental Response Compensation and Liability Act (CERCLA) (40 CFR 302): |
| Chemical Name | Hazardous Substances RQs | Extremely Hazardous Substances RQs | RQ |
| Hydrogen chloride | 5000 lb | 5000 lb | RQ 5000 lb final RQ RQ 2270 kg final RQ |
| Phosphoric acid | 5000 lb |  | RQ 5000 lb final RQ RQ 2270 kg final RQ |
| U.S. State Regulations |  |
| California Proposition 65 This product does not contain any Proposition 65 chemicals. |
| U.S. State Right-to-Know Regulations |
| "X" designates that the ingredients are listed on the state right to know list. |
| Chemical Name | New Jersey | Massachusetts | Pennsylvania | Illinois | Rhode Island |
| Hydrogen chloride | X | X | X | X | X |
| Phosphoric acid | X | X | X |  | X |
| U.S. EPA Label Information |  |
| EPA Pesticide Registration Number | Not applicable |
| 16. OTHER INFORMATION |
| NFPA | Health Hazard 3 | Flammability 0 | Instability 1 | Physical and Chemical Hazards - |
| HMIS | Health Hazard 3 | Flammability 0 | Physical Hazard 1 | Personal Protection X |
| Prepared By | Product Stewardship 23 British American Blvd. Latham, NY 12110 1-800-572-6501 |
| Issuing Date | 18-Apr-2013 |
| Revision Date | 18-Apr-2013 |
| Revision Note | Initial Release. |
| General Disclaimer The information provided on this SDS is correct to the best of our knowledge, information and belief at the date of its publication. The information given is designed only as a guide for safe handling, use, processing, storage, transportation, disposal and release and is not to be considered as a warranty or quality specification. The information relates only to the specific material designated and may not be valid for such material used in combination with any other material or in any process, unless specified in the text. |
| End of Safety Data Sheet |